## Slide 1
Engineer Name | Role in the organization | Date
Title will be updated by code
pydxAnalyze v1.0

## Slide 2: Index
1 | Capacity Analysis CPU Analysis Network Analysis
2 | Metrics Analysis CPU NFS/iSCSI Throughput Disk Throughput Network Throughput Internal NFS/iSCSI Latency Disk Latency NFS/iSCSI Server Operations per Second Disk IOPS Cache Hit Ratio

## Slide 3
Capacity Analysis

## Slide 4: Capacity Analysis
This section is intended to help with capacity and sizing analysis. CPU and Network graphs should be able to help you answer questions like:
What is the real utilization of my engine during one week?
What is the throughput/CPU available to add more objects (dSources/VDBs) on this engine?
Do I need to evacuate some of the objects (dSources/VDBs) from this engine?

## Slide 5: Capacity Analysis: CPU Capacity
On this section we review the 85% percentile of CPU. On the graph you can see 1 week data (one point per day). For capacity sizing we should use the 85% percentile, but on this graph we also add the min and max values for your reference.
While this analysis is useful for the majority of the cases, if there are heavy loads running in small periods of time, we may need to repeat this analysis per hour instead of per day to have a better understanding of the capacity status.
On some extreme cases we may also need to do use per second data instead of per minute data

## Slide 6: Capacity Analysis: Network Capacity
There is always a relation between network capacity and throughput in a Virtualization Engine. This graph shows 85% percentile of network throughput for one week (one point per day). A healthy Engine with 8vCPU without Jumbo Frames enables should be able to generate around 800 Mbytes/second total throughputs between all targets (NFS, iSCSI, etc...) and sources (SnapSync, LogSync, etc...).

## Slide 7
Metrics Analysis

## Slide 8: Metrics Analysis
This section is intended to help when there are performance issues or when we must have more information and details on what happened during a particular job/batch on the Delphix Engine ecosystem.

## Slide 9: Metrics : CPU
On this graph we see CPU data for one week with one-minute granularity. We also see the trend line for this data.
Averages should never be used for Capacity Planning. The metric that we should use for this is the 85% of the CPU showed in the first graph on this report.

## Slide 10: Metrics : NFS Throughput
On this graph we see weekly data for NFS Throughput with 1-minute granularity.
We use the NFS protocol to provision Oracle, Sybase and DB2 VDB’s. We also use NFS for Unstructured Files (virtualized folders).
This means this graph is showing only information of NFS traffic between the VDB’s and the Delphix Engine.
Other protocols (iSCSI, DSP, …) are not included on this graph.

## Slide 11: Metrics : iSCSI Throughput
On this graph we see weekly data for iSCSI Throughput with 1-minute granularity.
We use the iSCSI protocol to provision MSSQL VDB’s. This means this graph is showing only information of NFS traffic between the VDB’s and the Delphix Engine.
Other protocols (NFS, DSP, …) are not included on this graph.

## Slide 12: Metrics : Disk Throughput
On this graph we see 1-minute granularity Disk Throughput data from the Delphix Engine to the underlying storage layer.
We show here one week of data.
Comparing reads on this graph with reads on NFS/iSCSI Throughput graph we can estimate easily the Cache Hit Ratio happening on the Engine.

## Slide 13: Metrics : Network Throughput
On this graph we see 1-minute granularity Network Throughput through the Virtual Machine network interface that we use to run Delphix.
We show 1 week of data. Network Throughput includes all traffic between the Delphix Engine and all sources and targets. It’s basically all the traffic that go through the VMWare NIC and includes all protocols (NFS, iSCSI, DSP, etc…)

## Slide 14: Metrics : Internal NFS Latency
This graph shows latency inside the Delphix Engine NFS server stack with 1-minute granularity for one week.
For more information on the definition of this Latency please see the Appendix.
Write Latencies are normally higher than Read Latencies because in Delphix we don't cache writes, so we have to wait for the underlying storage to acknowledge the write.
If you want to know the full latency of a call, you will need to add the network latency from the Delphix Engine to the Target to the numbers showed on the graph.

## Slide 15: Metrics : Internal iSCSI Latency
This graph shows latency inside the Delphix Engine iSCSI server stack with 1-minute granularity for one week.
For more information on the definition of this Latency please see the Appendix.
Write Latencies are normally higher than Read Latencies because in Delphix we don't cache writes, so we have to wait for the underlying storage to acknowledge the write.
If you want to know the full latency of a call, you will need to add the network latency from the Delphix Engine to the Target to the numbers showed on the graph.

## Slide 16: Metrics : Internal Disk Latency
On this graph we see 1-minute granularity Disk Latency between the Delphix Engine and the underlying storage.
For more information on this metrics please see the Appendix.
We show 1 week of data.
In order to understand better what’s the range for this Delphix Engine it’s good to have the IO Report Card generated during the installation of the Engine handy, as storage thresholds change dramatically per client and per engine.

## Slide 17: Metrics : NFS Server Operations Per Second
On this graph we can see the number of operations per second on the Internal NFS stack.
Internal NFS stack is defined on the Appendix

## Slide 18: Metrics : iSCSI Server Operations Per Second
On this graph we can see the number of operations per second on the Internal iSCSI stack.
Internal iSCSI stack is defined on the Appendix

## Slide 19: Metrics : Disk IOPS
On this graph we see 1-minute granularity Disk IOPS generated on the underlying storage by the Delphix Engine.
We show 1 week of data.
This information is very useful to know when storage is shared and we need to have controls on it. For example if we are very aggressive with the parallel degree of our Snapsyncs, we can reduce IOPS by reducing the parallel degree of the Snapsync process.

## Slide 20: Metrics : Cache Hit Ratio
On this graph we can see an estimation of Cache Hit Ratio.
The values we are using are not exact and the results should be considered as just an estimation.
With this graph we should be able to have an estimation of how many of the reads requested from the VDBs are being served by memory and how many are served from storage.

## Slide 21
Appendix

## Slide 22: What is Internal Disk Latency ?
Development
Training
Test
Source
Internal Disk Latency is the latency of the storage attached to the Delphix Engine. Every time we do a read or write, Delphix will measure the latency of the call and register in the internal metrics.
Network
4 virtual iSCSI adaptors

## Slide 23: What is Internal NFS/iSCSI Latency ?
Development
Training
Test
Source
When a query is executed on a VDB on Development Target, the query will go through the network pipe to the Delphix Engine and once there, Delphix will serve the data requested from Cache or from Storage.
Internal NFS/iSCSI Latency is the time that Delphix will need to return the data to the network layer (the latency on the blue bubble).
If you want to know the full average latency from a VDB running on the Development target, you will have to add the network latency on the network layer from the Delphix Engine to the Development Target to the Internal NFS/iSCSI Latency. This information can be obtained doing a CLI network latency test.
Network
4 virtual iSCSI adaptors

## Slide 24: FAQ
Q – Why in an Engine that is provisioning Oracle and Sql Server databases, the Internal Latency for iSCSI is much higher than the Internal Latency for NFS (for reads)?
A – On Delphix, we measure iSCSI latencies in a way that does include queuing that results from TCP flow-control. This explains why the iSCSI read latencies are sometimes (or often) unusually high compared with the NFS read latencies.
Q – Is Internal Disk Latency always a subset of Internal NFS/iSCSI Latency?
A – Even though it may seem that this is the case, there are situations where this may not be true. One example is when large NFS/iSCSI I/Os are broken down into smaller disk I/Os. On that case a single NFS/iSCSI I/O latency served from disk would be the aggregate of all the underlying disk I/O latencies.
Disk latency is always a part of the NFS/iSCSI write because we never cache writes